## Slide 1: GRIT: Enhancing Multi-GPU Performance with Fine-Grained Dynamic Page Placement
Yueqi Wang*1, Bingyao Li*1, Aamer Jaleel2, Jun Yang1, Xulong Tang1
1University of Pittsburgh, 2NVIDIA

## Slide 2
Multi-GPU is Popular
Graph Processing
Datacenter Workloads
ChatGPT
DNN
[1] https://www.cerebras.net/blog/harnessing-the-power-of-sparsity-for-large-gpt-ai-models
Ever-growing application complexity and input dataset sizes.
Notes: Gpus are dominating and getting popular in many application fields, such as xxxx
as you might notice, the recent nvidia stock has a rocket spiking in the market.
However, we all witness that the applications are getting much more complicated and large-scale. the right figure using deep learning model as exmples and plots computing power and memory compacity requirement over years.
clearly, this is far beyond the capability of a single GPU .

## Slide 3
Multi-GPU is Popular
Ever-growing application complexity and input dataset sizes.
Graph Processing
Datacenter Workloads
ChatGPT
DNN
[1] https://www.cerebras.net/blog/harnessing-the-power-of-sparsity-for-large-gpt-ai-models
Multi-GPU is here ! (NVIDIA DGX, Intel Xe)

## Slide 4
UVM for Multi-GPU
Growing trend of multi-GPUs leveraging Unified Virtual Memory (UVM)
Global pointer to devices
Simplify development & deployment
Heterogeneity
Compatibility
GPU
Unified Memory
CPU
GPU
GPU
…
…
…
CPU
Notes: To harness the advantages of multi-GPU systems, increasing trend
provides single memory space for the applications
there are plenty of benefits from UVM.

## Slide 5
Chart: 
| 1-GPU | 2-GPUs | 4-GPUs
Series 1 | 1 | 1.85 | 2.35
Series 2 | 1 | 2 | 4
x
Data transfer
Address translation
……
2.4x
1.8x
x
x
x
x
[2] https://developer.nvidia.com/blog/easy-multi-gpu-deep-learning-digits-2/
Why performance gap:
Multi-GPU Scalability
NUMA data access
Notes: However, we all know there is no free-lunch. The UVM comes with its cons.
Delivered performance doesnot scale with the number of GPUs

## Slide 6
GPU0
Multi-GPU Page Placement Schemes
GPU1
UVM Driver
Page
Request
Migrate
1. On-Touch Migration: Request, Migrate.
Page
GPU0
GPU0
GPU0
GPU1
GPU1
Every memory access is local
Ping-Pong effect

## Slide 7
GPU0
Access counter
Multi-GPU Page Placement Schemes
2. Access Counter-based Migration: Reaching threshold, Migrate.
GPU1
UVM Driver
Page
Request
Migrate
+1
+1
+1
> Threshold
Page
Reduce Ping-Pong migration
GPU0
GPU1
Page
Substantial remote access

## Slide 8
Multi-GPU Page Placement Schemes
Protection
fault
3. Page Duplication: Read, Duplicate.
GPU0
GPU1
UVM Driver
Read
Duplicate
Page
Page
Reduce migration & remote access
GPU0
UVM Driver
GPU1
GPU2
Write
Page invalidation
Page
Page
Page
Significant collapsing overhead

## Slide 9
Performance of Page Placement Schemes
Chart: Normalized Performance
| BFS | BS | C2D | FIR | GEMM | MM | SC | ST
On-touch | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Access counter | 1.5699 | 1.1249 | 0.86209 | 0.52713 | 1.4667 | 1.6285 | 0.52627 | 1.07
Duplication | 2.1452 | 0.86965 | 0.66123 | 0.86922 | 2.3038 | 2.2498 | 0.80998 | 0.98462
No “one-size-fits-all” page placement scheme

## Slide 10
Page Access Characteristics
The page-sharing / read-write patterns vary within the same application
Chart: Time
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
GPU 1 | 0.923 | 0.05 | 0.33 | 0 | 1 | 1
GPU2 | 0.077 | 0.95 | 0.42 | 1
GPU3
GPU4 | 0.25
Private / Share
Chart: Time
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Write | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.20955 | 0.20955 | 0.20955 | 0.20955 | 0.20955 | 0.20955 | 0.20955 | 0.64985 | 0.64985 | 0.78189 | 0.78189 | 0.78189 | 0.78189 | 0.78189 | 0.78189 | 0.78189 | 0.78189 | 0.78189 | 0.78189 | 0.91904 | 0.55804 | 0.55804 | 0.55804
Read | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.79045 | 0.79045 | 0.79045 | 0.79045 | 0.79045 | 0.79045 | 0.79045 | 0.35015 | 0.35015 | 0.21811 | 0.21811 | 0.21811 | 0.21811 | 0.21811 | 0.21811 | 0.21811 | 0.21811 | 0.21811 | 0.21811 | 0.080957 | 0.44196 | 0.44196 | 0.44196
Read / Write
A dynamic page placement scheme that can accommodate variations in page access characteristics

## Slide 11
Problem:
Problem Summary
  No “one-size-fits-all” page placement scheme
Goal:
  Effectively reduce NUMA overhead in multi-GPU by determining
  page placement scheme at runtime
  Delivered performance is constrained by NUMA overhead

## Slide 12
GRIT (Fine-GRained dynamIc page placemenT)
Dynamically determine page placement scheme at runtime
Scheme change
metric
Notes: propose GRIT,
to dynamically determine scheme
when the scheme is identified as improper and should change, so in other words, it’s important to know the metric of scheme change

## Slide 13
GRIT – Scheme Change Metric
GPU0
UVM Driver
Request
local page fault
Write
page protection fault
Page
Page duplication should
be avoided
Current scheme is unsuitable
UP
UP
Indicator: Number of page faults (local page fault & page protection fault)
Notes: suppose using on-touch as default scheme,
indicate multiple gpu access the same page, current on-touch is not suitable, maybe a page duplication is suitable to enable pages presented in several devices.
high write collapsing overheads should be avoided.
we employ the page fault as an indicator to trigger the scheme change

## Slide 14
GRIT: Dynamic Page Placement Scheme
How to track information ?
Dynamically determine page placement scheme at runtime
Scheme change
metric
Fault-Aware Initiator

## Slide 15
GRIT – Page Attribute Table and Cache (PA-Table & Cache)
CPU Memory
PA-Table |  | 
VPN | Fault Counter | Read/Write
0xA00 | 10 | 0
0xA01 | 01 | 1
… | … | …
PA-Cache
VPT | FC | R/W
… | … | …
… | … | …
… | … | …
… | … | …
Way 0
VPT | FC | R/W
… | … | …
… | … | …
… | … | …
… | … | …
Way 3
…
Write allocate
Write back
Additional memory access
Facilitate lookup
Notes: design page attributes and track the number of page faults read/write. when a page fault received by UVM driver, it need to check the PA-table. However, each fault will check table in memory
hottest, latest

## Slide 16
GRIT: Dynamic Page Placement Scheme
How to track information ?
Scheme change
metric
Fault-Aware Initiator
PA-Table &
PA-Cache
Dynamically determine page placement scheme at runtime
Which scheme to change to ?

## Slide 17
GRIT – Which Scheme
Get access information from PA-Table /PA-Cache
FC Reach threshold?
Access-counter
True
False
All read?
Duplication
True
Change Scheme
XD | Unused Bits (UB) | 4 KB Page Frame Number (PFN) | UB | Scheme Bits
63 62:54 53:52 51:12 11 10:9
Scheme information is stored in host PTE.
On-touch

## Slide 18
GRIT: Dynamic Page Placement Scheme
How to track information ?
Scheme change
metric
Fault-Aware Initiator
PA-Table &
PA-Cache
Dynamically determine page placement scheme at runtime
Which scheme to change to ?
Scheme Decision Mechanism
Notes: three technique works together to achieve dynamic page placement

## Slide 19
GRIT: Dynamic Page Placement Scheme
Chart: Normalized performance
| BFS | BS | C2D | FIR | GEMM | MM | SC | ST
On-touch | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Access counter | 1.5699 | 1.1249 | 0.86209 | 0.52713 | 1.4667 | 1.6285 | 0.52627 | 1.07
Duplication | 2.1452 | 0.86965 | 0.66123 | 0.86992 | 2.3038 | 2.2498 | 0.80998 | 0.98462
GRIT-Dynamic | 1.7303 | 1.0434 | 1.1179 | 1 | 2.6273 | 1.9977 | 1 | 1.0357
Performance gap due to improper scheme before trigger scheme change
Notes: Is this good enough to solve the problem/is the problem completely resolved? the answer is Not really.
As one can observe, while GIRT-dynamic performs good in application such as c2D, it is worse than duplication in application such mm.
Why is that? well, our approach uses the page fault number to capture and change the scheme, it needs to accumulate the fault counts to reach the threshold. This is, kind of we call learning phase. since for each page, we need to learn the behavior individually in page grunularity, this learning overheads can dominating and offset the performance gains.

## Slide 20
Page Attributes Characterization
The neighboring pages tend to exhibit similar access attributes
Proactively determine page placement scheme
for neighboring pages
Notes: Then what can we do. Well, we can use larger granularity to amortize the learning overheads. But is there any opportunity for that?
look from bottom to top, the attributes of specific pages change over time
even though the attributes changes, neighboring pages exhibit similar page attributes.

## Slide 21
GRIT: Neighboring-Aware Prediction
Proactively decide
neighboring scheme
Neighboring-Aware Prediction
How to track information ?
Scheme change
metric
Fault-Aware Initiator
PA-Table &
PA-Cache
Dynamically determine page placement scheme at runtime
Which scheme to change to ?
Scheme Decision Mechanism
Notes: neighboring aware prediction

## Slide 22
GRIT: Neighboring-Aware Prediction
00
00
00
00
01
01
01
10
0xF000
0xF001
0xF002
0xF003
0xF004
0xF005
0xF006
0xF007
Page Table
VPN
Scheme
00
00
00
00
01
01
01
00
00
00
00
00
00
00
00
00
Promote
32KB page group
XD | Unused Bits (UB) | Group Bits
63 62:54 53:52
…
256KB page group
Recursively
Promote

## Slide 23
GRIT – Put All Together
Fault reach threshold？
UVM Driver
No, resolve fault
resolve fault
Yes,
change scheme

## Slide 24
Methodology
Simulator: MGPUSim [ISCA 19’]
Workloads: 8 applications from Hetero-Mark, AMDAPPSDK , SHOC, and DNN Mark benchmark suites, including random, adjacent, and scatter-gather access patterns.
Detailed page placement scheme modeling in paper

## Slide 25
Evaluation – Overall Performance
GRIT achieves 60%, 49%, and 29% performance improvement compared to uniformly employing on-touch, access counter-based, and page duplication scheme.
Chart: Normalized performance
| BFS | BS | C2D | FIR | GEMM | MM | SC | ST | Ave.
On-touch | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Access counter | 1.5699 | 1.1249 | 0.86209 | 0.52713 | 1.4667 | 1.6285 | 0.52627 | 1.07 | 1.0969
Duplication | 2.1452 | 0.86965 | 0.66123 | 0.86992 | 2.3038 | 2.2498 | 0.80998 | 0.98462 | 1.3718
GRIT | 2.1042 | 1.2296 | 1.1182 | 1 | 2.71 | 2.4592 | 1.0166 | 1.16 | 1.5937

## Slide 26
Evaluation – Scheme Breakdown
GRIT is able to distinguish page attributes and consistently select
the most suitable scheme accordingly.
Chart: Scheme percentage
| BFS | BS | C2D | FIR | GEMM | MM | SC | ST
On-touch | 0.31885 | 0.40016 | 0.82567 | 1 | 0.42034 | 0.35199 | 1 | 0.36473
Access counter | 0.091947 | 0.53193 | 0.051053 | 0 | 0.0041728 | 0 | 0 | 0.22735
Duplication | 0.58921 | 0.067905 | 0.12327 | 0 | 0.57549 | 0.64801 | 0 | 0.40792

## Slide 27
Summary
Problem: NUMA overheads in multi-GPU systems
GRIT:
Dynamic page placement scheme determines schemes in a fine-grained manner
Neighboring-aware prediction proactively determines adjacent page scheme
Improves performance by 60% on average.
No “one-size-fits-all” page placement scheme

## Slide 28: GRIT: Enhancing Multi-GPU Performance with Fine-Grained Dynamic Page Placement
Thanks! Q&A
Yueqi Wang*1, Bingyao Li*1, Aamer Jaleel2, Jun Yang1, Xulong Tang1
1University of Pittsburgh, 2NVIDIA

## Slide 29
GRIT (Fine-GRained dynamIc page placemenT)
Dynamically determine scheme at runtime
Proactively decide neighboring scheme
Key Observations:
  Page-sharing patterns vary among/within application
1
  Neighboring pages exhibit similar access attributes
2