## Slide 1: IDYLL: Enhancing Page Translation in Multi-GPUs via Light Weight PTE Invalidations
Bingyao Li1, Yanan Guo1, Yueqi Wang1, Aamer Jaleel2, Jun Yang1, Xulong Tang1
1University of Pittsburgh, 2NVIDIA

## Slide 2
Ever-growing application complexity and input dataset sizes
Multi-GPU is Popular
Multi-GPUs provide aggregated memory capacity
Unified virtual memory simplifies application deployment
Multi-GPU is here ! (NVIDIA DGX, Intel Xe)
Graph Processing
Datacenter Workloads
ChatGPT
DNN

## Slide 3
Multi-GPU Scalability
Chart: 
| 1-GPU | 2-GPUs | 4-GPUs
Series 1 | 1 | 1.85 | 2.35
Series 2 | 1 | 2 | 4
x
NUMA data access
Data transfer
Address translation
……
2.4x
1.8x
x
x
x
x
[1] https://developer.nvidia.com/blog/easy-multi-gpu-deep-learning-digits-2/
Why performance gap:

## Slide 4
Multi-GPU Scalability
Chart: 
| 1-GPU | 2-GPUs | 4-GPUs
Series 1 | 1 | 1.85 | 2.35
Series 2 | 1 | 2 | 4
x
NUMA data access
Data transfer
Address translation
2.4x
1.8x
x
x
x
x
[1] https://developer.nvidia.com/blog/easy-multi-gpu-deep-learning-digits-2/
Why performance gap:
Occupies 30%-80% of execution time
(T. Allen et al. [SC’21], B.Li et al. [MICRO’21],
S. Shin et al. [MICRO’18])

## Slide 5
Address Translation in Multi-GPU
memory
Page
GPU0
CPU
UVM driver
GPU1
GMMU
Device Memory
Compute Unit
L1 TLB
memory
Page
GPU1
L2 TLB
Compute Unit
L1 TLB
Page
Page Table
invalid
Page Table
remote
demand TLB miss request
far fault
remote mapping
Reduce far faults and page migration
On critical path
Long latency handling

## Slide 6
Page Sharing Characterization
Chart: Distribution of accesses referencing shared pages
| MT | MM | PR | ST | SC | KM | IM | C2D | BS
One GPU | 147648 | 42341 | 8892796 | 10 | 5193660 | 186375 | 7759997 | 39824 | 202700
Shared by 2 | 147456 | 0 | 166488 | 0 | 11979659 | 0 | 1562780 | 82049 | 416827
Shared by 3 | 0 | 0 | 0 | 308312 | 6357922 | 0 | 1035 | 6076 | 208179
Shared by 4 | 0 | 1470504 | 120432434 | 525630 | 35768996 | 1397871 | 2884103 | 21273 | 247449
Significant page sharing among multiple GPUs
Reduce NUMA data access -> Frequent page migration
Observation:

## Slide 7
Page Migration with Remote Mapping
GPU0
Page Table
local
Page
GPU1
Page Table
remote
Page
GPU2
Page Table
remote
Page
GPU3
Page Table
Page
UVM Driver
Initiate migration
Broadcast to every GPU
Each GPU
invalidate TLB & PTE
Update page table
local
Page

## Slide 8
Problem of Existing Page Migration
GPU0
Page Table
local
Page
GPU1
Page Table
remote
Page
GPU2
Page Table
remote
Page
GPU3
Page Table
Page
UVM Driver
Initiate migration
Broadcast to every GPU
Each GPU
invalidate TLB & PTE
Page
Update page table
remote
Unnecessary
Additional memory accesses

## Slide 9
PTE Invalidation Characterization
Substantial PTE invalidation requests
PTE invalidations accounts for a quarter of total requests to the page walker.
Observation:
Chart: 
| MT | MM | PR | ST | SC | KM | IM | C2D | BS | Ave.
TLB miss requests | 216098 | 206108 | 1361029 | 294487 | 196319 | 349581 | 120048 | 93428 | 509916 | 1
Necessary invalidation requests | 9861.0938 | 68908 | 864548 | 62478 | 33940 | 98180 | 1722 | 5136 | 39054.4346 | 0.25133
Unnecessary invalidation requests | 5165.9062 | 36524 | 120956 | 14394 | 21092 | 28588 | 1582 | 3712 | 20321.5654 | 0.10867
27.2%

## Slide 10
PTE Invalidation Characterization
Substantial PTE invalidation requests
PTE invalidations accounts for a quarter of total requests to the page walker.
One-third of PTE invalidations broadcasted are unnecessary.
Observation:
Chart: 
| MT | MM | PR | ST | SC | KM | IM | C2D | BS | Ave.
TLB miss requests | 216098 | 206108 | 1361029 | 294487 | 196319 | 349581 | 120048 | 93428 | 509916 | 1
Necessary invalidation requests | 9861.0938 | 68908 | 864548 | 62478 | 33940 | 98180 | 1722 | 5136 | 39054.4346 | 0.25133
Unnecessary invalidation requests | 5165.9062 | 36524 | 120956 | 14394 | 21092 | 28588 | 1582 | 3712 | 20321.5654 | 0.10867
32%

## Slide 11
PTE Invalidation Characterization
Substantial PTE invalidation requests
PTE invalidations accounts for a quarter of total requests to the page walker.
One-third of PTE invalidations broadcasted are unnecessary.
Observation:
Chart: 
| MT | MM | PR | ST | SC | KM | IM | C2D | BS | Ave.
TLB miss requests | 216098 | 206108 | 1361029 | 294487 | 196319 | 349581 | 120048 | 93428 | 509916 | 1
Necessary invalidation requests | 9861.0938 | 68908 | 864548 | 62478 | 33940 | 98180 | 1722 | 5136 | 39054.4346 | 0.25133
Unnecessary invalidation requests | 5165.9062 | 36524 | 120956 | 14394 | 21092 | 28588 | 1582 | 3712 | 20321.5654 | 0.10867
32%
How is performance impacted by PTE invalidations?

## Slide 12
Invalidation Overhead
Contend with demand TLB miss request.

## Slide 13
Invalidation Overhead
Without the interference of invalidation requests, the demand TLB miss request latency reduced by 55.8%.
Contend with demand TLB miss request.
GMMU
L2 TLB
Demand TLB miss request
UVM driver
PTE invalidation request

## Slide 14
Invalidation Overhead
Extra latency for waiting page to be migrated.

## Slide 15
Invalidation Overhead
30% of total page migration time is spent on waiting page to be migrated.
GPU0
Page Table
local
Page
GPU1
Page Table
remote
Page
Invalidation complete ! Migrate !
Request
Waiting…
Access !
Page
Extra latency for waiting page to be migrated.
local

## Slide 16
Problem Summary
Address the overheads associated with PTE invalidations
Problem:
PTE invalidations
Unnecessary broadcast
Contend with the demand TLB miss requests
In-PTE Directory Invalidation
Lazy Invalidation
In-PTE DirectorY and Lazy InvaLidation (IDYLL)

## Slide 17
XD | Unused Bits | 4 KB page frame | UB | G | PAT | D | A | PCD | PWT | R/W | U/S | V
63 | 62 52 | 51 12 | 11 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
access bits
IDYLL : In-PTE Directory Invalidation
Host side page table
CR3
Host-side page table holds all up-to-date translations in all GPU.

## Slide 18
IDYLL : In-PTE Directory Invalidation
CPU
UVM driver
Page Table
62 52 |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 0 | 0 | 0
GPU0
Page Table
invalid
GPU1
Page
GPU2
Page Table
remote
First access request
1
local
1
At the time of first far fault, the access bit is set to 1.
First access request
Page Table
remote
far fault
far fault

## Slide 19
IDYLL : In-PTE Directory Invalidation
CPU
UVM driver
Page Table
62 52 |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 0 | 
GPU0
Page Table
local
GPU1
GPU2
Page Table
remote
1
1
Send invalidations only to GPUs with access bits set to 1.
0
0
Initiate migration
Page Table
remote

## Slide 20
IDYLL : Lazy Invalidation
Invalidation Request Merging Buffer (IRMB)
GPU
GMMU
Device Memory
L2 TLB
Page Table
remote
UVM driver
IRMB
In-PTE Directory Invalidation -> unnecessary invalidations
Still substantial valid translation mappings
temporally buffer and batch invalidation requests and lazily update the local page table.

## Slide 21
IDYLL : Lazy Invalidation
GPU
GMMU
L2 TLB
Device Memory
Page Table
remote
UVM driver
IRMB
invalidation
IRMB :
The invalidation request inserted into IRMB instead of performing invalidation immediately.
batching
Nearby invalidations are merged into one entry and batched write back to page table
Serve as indicator of invalid PTE that, if hit in IRMB, can bypass local page table walk
bypass
hit

## Slide 22
Methodology
Simulator: MGPUSim [ISCA 19’]
Workloads: 9 applications from Hetero-Mark, AMDAPPSDK , SHOC, and DNN Mark benchmark suites.
Hardware setup:
 | Configuration
L2 TLB | 512 entries, 16 way, CUs shared
Page table walk | GMMU 8 shared page table walker, 100-cycle latency per level
Page table cache | 128 entries shared across page table walker
Access counter threshold | 256

## Slide 23
Evaluation
IDYLL achieves an average of 69.9% performance improvement.
Chart: Normalized performance
| MT | MM | PR | ST | SC | KM | IM | C2D | BS | Ave.
IDYLL | 1.3863 | 1.3077 | 2.67 | 1.9489 | 1.5219 | 1.7178 | 1.6853 | 1.746 | 1.3074 | 1.699
Zero-Latency Invalidation | 1.548 | 1.5892 | 2.92 | 1.6229 | 1.4201 | 1.6925 | 1.5814 | 1.8021 | 1.3796 | 1.7284
69.9%

## Slide 24
Evaluation
Chart: Normalized performance
| MT | MM | PR | ST | SC | KM | IM | C2D | BS | Ave.
IDYLL | 1.3863 | 1.3077 | 2.67 | 1.9489 | 1.5219 | 1.7178 | 1.6853 | 1.746 | 1.3074 | 1.699
Zero-Latency Invalidation | 1.548 | 1.5892 | 2.92 | 1.6229 | 1.4201 | 1.6925 | 1.5814 | 1.8021 | 1.3796 | 1.7284
IDYLL nears zero-latency invalidation performance.

## Slide 25
More in the Paper
Performance sensitivity to :
IRMB size
Number of page table walk threads
L2 TLB size
Number of GPUs
Number of unused bits
Access counter threshold
Detailed lookup process of IDYLL
Experiment configurations
Performance improvement breakdown
Comparison with Large Page, Page Replication, State-of-the-art

## Slide 26
Problem: PTE invalidation overheads in multi-GPU systems.
IDYLL:
In-PTE Directory reduces unnecessary PTE invalidations
Lazy Invalidation amortizes and minimizes PTE invalidation overheads
Improves performance by 69.9% on average.
Unnecessary PTE invalidation broadcast
Contend with demand TLB miss request
Summary

## Slide 27: IDYLL: Enhancing Page Translation in Multi-GPUs via Light Weight PTE Invalidations
Bingyao Li1, Yanan Guo1, Yueqi Wang1, Aamer Jaleel2, Jun Yang1, Xulong Tang1
1University of Pittsburgh, 2NVIDIA
Thanks! Q&A
Email: bil35@pitt.edu